## Slide 1: Group # 19
Michelle SID: 604970379
Chester SID: 104979768
Myles SID: 205868607

## Slide 2: Summarized Numbers
Our design did synthesize however we could not verify post synthesis working of the design with .sdf
Technology | Synopsys 32nm
Total Area (A) | 0.475 mm2
Total Power (PT) | 386 mW
Clock Period (TCLK) | 3.5 ns
Number of Clock Cycles (NCLK) | 1979
Energy/Operation (EOP) | 2.67 µJ
Energy - Area Product (EOP x A) | 1.268 µJ*mm2

## Slide 3: Design Features & Optimizations
To reduce area, we reused 1 neuron
Used 4 pipelined multipliers
Sum is accumulated over 196 batches of inputs and weights
Tested different combinations of batch sizes & accumulators to find one with optimal area x energy
Multiplier
Adder
reg
out
pixels
weights
PipelinedMultiplyAccumulate
PipelinedMultiplyAccumulate
PipelinedMultiplyAccumulate
+
+
+
+
TreeAdder
Neuron
196p
196w
196p
196w
784p
7840w
out